## Slide 1: MT6293 MP1 SQC Workshop 93 Call Domain Selection
  15 May 2017

## Slide 2: Outline
Introduction
Architecture
ADS Overview
Log Analysis & Case Study Example

## Slide 3: Introduction
90/91/92
  MD1 and MD3 are separated, VDM only decides call domain selection for IMS and CS call of MD1.
  C2K domain selection is handled by AP. AP will send AT cmd request directly to MD3 (CVAL) for C2K call.
93
  MD1 and MD3 are merge into a single MD.
  VDM decides call domain for IMS and CS and C2K call.
  Call related AT cmd/URC
    For AP: AT cmd/URC merged as used in MD1
      For example: ATD, +ECPI…
    Below ATCI/L4C、CVAL: remain the same
      For example: for GSM still ATD; for C2K still AT+CDV
    Translated in VDM and L4BCC

## Slide 4: Architecture
Android
Telephony Framework
VoLTE UA
IMCB
(IMS Core Bearer)
IMSA
(IMS
Adaptor)
RIL
Dialer
ATCI / L4C Group
LTE NAS
LTE AS
3G AS
2/3G NAS
2G AS
Android
Mobile Data Service
IMC
(IMS Core)
VDM
(Voice Domain Manager)
IMSP
IMS server
AP
MD1
CVAL
CSS
C2K AS
ILM
AT in ILM
SIP
Android
Telephony Framework
VoLTE UA
IMCB
(IMS Core Bearer)
IMSA
(IMS
Adaptor)
RIL
Dialer
ATCI / L4C Group
LTE NAS
LTE AS
3G AS
2/3G NAS
2G AS
Android
Mobile Data Service
IMC
(IMS Core)
VDM
(Voice Domain Manager)
ATP
IMS server
AP
MD
CVAL
CSS
C2K AS
L4BCC / L4B Group
MD3
90/91/92
93

## Slide 5: Architecture
Interface changes
  New module: L4BCC, adaption module between VDM and ATCI/CVAL
  After Gen93, VDM will use ILM to request CS/C2K call by sending different ILM groups to L4BCC.
  ILM naming can distinguish the request is for CS or C2K call, for example:
    CS: MSG_ID_VDM_L4B_CS_CC_MO_CALL_REQ
    C2K: MSG_ID_VDM_L4B_C2K_CC_MO_CALL_REQ
  L4BCC will interpret ILM as AT command and forward it to corresponding ATCI or CVAL, for example
    CS: ATDXXXXX; to ATCI
    C2K: AT+CDV=XXXXX to CVAL

## Slide 6: ADS Overview – normal call
User Dial Call
apply hVoLTE?
hVoLTE Selection Algoritm
Normal Selection Algorithm
Yes
No
CS
Reject
Cellular IMS
WIFI IMS
C2K
Reject
Cellular IMS
WIFI IMS
Check C2K if rat_mode has C2K

## Slide 7: ADS Overview – normal call
apply hVoLTE?
  C2K CS is registered => regardless following condition
  If one the following condition is true => no; otherwise, yes
    l4c_query_hvolte_enable_status() == HVOLTE_DISABLE
      Depends on nvram_ef_hvolte_e911_struct->hvolte_enable
        CT: HVoLTE_MANUAL_MODE
        VzW: HVoLTE_AUTO_MODE
        Others: HVoLTE_DISABLE
    rat_mode not contain RAT_C2K
    is not in home country
      from GMSS reported RAT change indication +ERPRAT
    CS registration status is roaming

## Slide 8: ADS Overview – emergency call
User Dial ECC Call
emc scan enable?
E911 Selection Procedure
Emergency Selection Algorithm
Yes
No
CS
Reject
Cellular IMS
WIFI IMS
C2K
Reject
Cellular IMS
WIFI IMS
CS
Need AP change to
global rat, and redial
Check C2K if rat_mode has C2K
Send EMC_SERVICE_SCAN_REQ (AT+EMCSS) to request L4C/GMSS for available ECC rat

## Slide 9: ADS Overview – emergency call
emc scan enable?
  nvram_ef_vdm_ads_profile_struct-> nvram_vdm_common_profile_struct-> allow_global_emc_scan
    CT, VzW, Sprint: 1
    Others: 0

## Slide 10: Log Analysis
Keyword (MD log, PS)
  primitives
    MSG_ID_VDM_IMC_IMS_CC_MO_CALL_REQ
    MSG_ID_VDM_L4B_CS_CC_MO_CALL_REQ
    MSG_ID_VDM_L4B_C2K_CC_MO_CALL_REQ
    MSG_ID_VDM_ATP_EMC_SERVICE_SCAN_REQ
    MSG_ID_VDM_ATP_EMC_SERVICE_IND
    MSG_ID_VDM_ATP_SND_ECPI_CALL_RELEASE_REQ
  trace prefix
    [VDM] hVoLTE
    vdm_ads_select_domain
    ADS algo
    SSAC ctrl
    Timer:
Regular exp (MD log, PS)
  ^MSG_ID_VDM_ATP_EMC|MSG_ID_VDM_.*(IMC|L4B).*CALL_REQ|ATP_SND_ECPI_CALL|\[VDM\] hVoLTE|\[VDM ADS\].*(vdm_ads_select_domain|ADS algo|SSAC ctrl|timer:)

## Slide 11: Log Analysis – normal call
apply hVoLTE for normal call
  C2K CS is registered
  C2K CS is not registered, but all condition check ok
not apply hVoLTE for normal call
    one of the following reason
    followed by
[VDM] hVoLTE_enable : C2K CS reigstered [VDM ADS] vdm_ads_select_domain_for_normal_for_hvolte()
[VDM ADS] vdm_ads_select_domain_for_normal_for_hvolte()
[VDM] hVoLTE_disable : l4c_query_hvolte_enable_status = HVOLTE_DISABLE [VDM] hVoLTE_disable : rat_mode not contain C2K [VDM] hVoLTE_disable : is not home by +EPRAT [VDM] hVoLTE_disable : roaming
[VDM ADS] vdm_ads_select_domain_for_normal()

## Slide 12: Log Analysis – normal call
ADS algo: C2K CS domain is allowed to use (a candidate for ADS)
reason
  hVoLTE manual mode with hvolte_mode=LTE only
  C2K RAT disable
  ADS mode = xxxx
  There is at least an ongoing IMS call
Debug:
OP load: check VoLTE icon should off
OM load: if CT sim, check with L4 owner Kuan-wei Chen
ADS algo: C2K CS domain not allowed (reason)
Call is allowed to make in C2K CS domain

## Slide 13: Case study – normal call example 1
not apply hVoLTE for normal call
  selects CS

## Slide 14: Case study – normal call example 2
apply hVoLTE for normal call
  selects C2K CS

## Slide 15: Case study – normal call example 3
apply hVoLTE for normal call
  cannot select C2K CS due to hvolte_mode: LTE only
    Need check VoLTE icon or L4 owner

## Slide 16: Log Analysis – emergency call
emc scan enable for ECC call?
  allow_global_emc_scan= ture
  allow_global_emc_scan= false
[VDM ADS] vdm_ads_select_domain_for_emergency_for_hvolte()
[VDM ADS] vdm_ads_select_domain_for_emergency()

## Slide 17: Log Analysis – emergency call
  allow_global_emc_scan=ture
  VDM will send EMC_SERVICE_SCAN_REQ (AT+EMCSS) toward L4C/GMSS for available rat to attempt E911
  L4C/GMSS will response
    available rat for VDM to attempt ECC or
      LTE/GSM/UMTS/C2K
    RAT_NONE for AP to change to global rat and redial
B
B
A

## Slide 18: Case study – emergency call example 1
  allow_global_emc_scan= false
  selects CS

## Slide 19: Case study – normal call example 2
  allow_global_emc_scan= true
    L4C/GMSS response with RAT_C2K, VDM selects C2K CS

## Slide 20: Case study – normal call example 3
  allow_global_emc_scan= true
    L4C/GMSS response with RAT_NONE, VDM reject to AP with cause 2003 for AP to change to global mode and redial by ATDER="<call_number>”,<call_id>