## Slide 1: D2/DDM
  17 April 2017

## Slide 2
IMCB
Android Framework
L4
IMC
ATP
AP
MD
IMSM
AT in ILM
AT
TTY Dev.
TTY Dev.
SIM
SIMMNGR
VOLTE stack/UA
SIM
AT/URC
(Proprietary )
TCP/IP
Stack
IMCB_IMSM
Interface
MD Application
IMS
Common Data Interface
AP branch
XCAP
BIP
IWLAN
NetAgent
DDM
ePDGa
L4BPDN
RILD
Vendor-ril
RIL Request
MOD_IMSM
D2
(task)

## Slide 3
L4
ATP
AP
MD
AT in ILM
AT
TTY Dev.
TTY Dev.
AT/URC
(Proprietary )
TCP/IP
Stack
BIP
(MD APP@MD)
IWLAN
DDM
ePDGa
L4BPDN
D2PM
D2CM
D2 Task
D2AM
IMSM
(MD APP@AP)
MD Application
RILD
NetAgent
TCP/IP
Stack
Common Data Interface
D2Adapter
D2AT
D2IMSM
L4BNW

## Slide 4: Modules
TASK | Modules | Features
D2 | D2AT (You-Ren Chen) | AT command interface support (from AP) PDP context cache (Legacy AT command) e.g., AT+CGDCONT, AT+CGDSCONT CID remapping Post CID allocation for legacy AT command
 | D2CM (Chia-yu Ku) | Common data interface Multi-user support AP users use the AP TCP/IP stack MD users use the MD TCP/IP stack MD users use the AP TCP/IP stack Network interface manager AP CCMNI MD TCP/IP stack device IP address manager IPv4/IPv6 address RS/RA IP changed
 | D2PM (Chia-yu Ku) | APN information CID allocation PDN activation/deactivation/reuse
 | D2AM (Yts Chen/Chang-Yen Chih) | IA selection IA definition IA cache PS attach/detach control EDALLOW for MPS/SPS
DDM | DDM (Dennis Tsai) | IPv4v6 fallback PDN-layer data retry