## Slide 1: MD TCPIP Stack Debugging Guide - 20170718
WSP/SE7/SD1
Christine-PL Tsai
7/18/2017

## Slide 2: Outline
List:
  Why MD TCP/IP stack in MD?
  MD TCP/IP architecture.
  Data transferring flow.
  Tips to debug.
  Summary.

## Slide 3: Why TCP/IP Stack in MD?
Security concern
  BIP (Bearer Independent Protocol) needs to be hidden in modem side.
The BIP needs TCP/IP protocol stack to process data.
CAT application
CAT server(e.g. web server)
Terminal Server
Terminal application
UICC
Terminal
Remote Server
BIP Protocol
TCP / UDP Transport Layer
BIP Layer
Http client (e.g. browser)
Terminal server mode
UICC Server mode
BIP communication
Notes: Security concern: While establishing PDN, related parameters are plain and might be hacked in AP.
We need to provide networking stack in MD!
Start on Gen93.
UICC=SIM

## Slide 4: Modules Interact with TCP/IP Stack
TCP/IP Stack
DHL/
ELT
L5/D2
MD Users
Nucleus OS
IPcore
Logging and debugging
Handling PDN in MD
Use MD networking
Data path & filter
Existing OS API

## Slide 5
MD TCP/IP Architecture
IPCore
TCP
UDP
ICMP
RAW
...
NAL (socket, NW utilities)
Network APP
MD User
TCP/IP stack
Filter Queue
device
RX
TX
D2CM
STK driver (for IPcore)
DHL
STKDEMX
STKEVTD
STKBUF
...
STKBRG
StkIF
StkIF
StkIF
...
RX
TX
L5/D2
D2PM
ELT
1
2
3
4
5
Establish PDN
routing
Debugging
Using NAL API
Nucleus OS
Kernel API
TCP/IP KAL tasks

## Slide 6: General MD Networking Application Flow
Establish
PDN
Disconnect
PDN
NAL networking interface
One MD network application (e.g., BIP) can setup one or more sockets with different settings.
Socket
Setup
Add
Filter
Send/
Receive
Resource
Cleaning
Socket
Setup
Add
Filter
Send/
Receive
Resource
Cleaning
…
MD network applications
Notes: Such as different ports, different remote IP address on one PDN.

## Slide 7: Establishing PDN --- MD Stack Interface
device
StkIF
StkIF
StkIF
D2CM
...
L5/D2
D2PM
StkIF
StkIF
IPv4 PDN
IPv6 PDN
IPv4
IPv6
StkIF
IPv4 PDN
IPv6 PDN
IPv4
IPv6
StkIF
IPv4v6 PDN
IPv4
IPv6
1
2
3
Similar to IPCore, the mapping relationship between StkIF and PDN shown in the below.
v4 or v6
standalone
v4 and v6
fallback
v4 and v6
Notes:     For each PDN establishment, we setup one corresponding MD interface; For the disconnection, we will down the interface.
  That is, two PDNs will be mapped to the same STK device.
Special case: If the APN has v4v6 fallback, two PDNs will mapped to the same STK device respectively.

## Slide 8: PDN Messages for Establishment
D2
Network APP
STK device
Establish PDN
STKBRG
1
2
STK driver
(for IPcore)
4
3
    MSG_ID_D2CM_STKBRG_ESTABLISHPDN_REQ
    MSG_ID_D2CM_STKBRG_ESTABLISHPDN_CNF
This message includes networkrelated parameters, such as PDN IP address, MTU, interface ID.
TCP/IP stack will update these parameters to STK interface.
6
    MSG_ID_D2CM_STKBRG_DISCONNECTION_REQ
This message includes interface ID
8
    MSG_ID_D2CM_STKBRG_DISCONNECTION_CNF
7
TCP/IP stack close the STK interface by interface ID.
StkIF
StkIF
StkIF
Disconnect PDN
5

## Slide 9: PDN --- PDN Messages for Update
Interface change:
    MSG_ID_D2CM_STKBRG_IFCHANGE_REQ
    MSG_ID_D2CM_STKBRG_IFCHANGE_CNF
  D2 would send changes (e.g., IP change) happening in PDN to STKBRG.
Global Address (with v6 address):
    MSG_ID_D2CM_STKBRG_GLBADDR_REQ
    MSG_ID_D2CM_STKBRG_GLBADDR_CNF
  This message is used to update global address, and it’s usually be sent after D2 finishes using IPv6 global address.
Notes: This messages will carry similar message as establishment one.
TCP/IP stack will update these parameters to the STKIF.
    TCP/IP stack will update this IPv6 address to the STKIF.

## Slide 10: Network Abstraction Layer
An abstraction layer to isolate the internal stack and MD users.
Also help users to configure the filters to IPCore easily.
Common Socket |  |  | Utility | Filter
nal_socket | nal_recvmsg | nal_fd_reset | nal_inet_pton | nal_add_filter
nal_bind | nal_getsockopt | nal_fd_set | nal_inet_ntop | nal_delete_filter
nal_get_sock_name | nal_setsockopt | nal_select | nal_htons | nal_update_filter
nal_connect | nal_shutdown |  | nal_ntohs | 
nal_is_connected | nal_close_socket |  | nal_htonl | 
nal_send | nal_fcntl |  | nal_ntohl | 
nal_recv | nal_fd_check |  |  | 
nal_send_to | nal_fd_init |  |  | 
nal_recv_from |  |  |  | 
nal_sendmsg |  |  |  | 
N
A
L
Notes: Error code translation, user statistics, …

## Slide 11: NAL User Guide
Link:
  Continue updating if any.
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/Gen93_NAL_Programming_Guide.docx
    Socket API description, socket usage flow, error code, …
Notes: Error code translation, user statistics, …

## Slide 12: General NAL Socket Usage [UDP]
UDP, connectionless:
  An example to connect to remote server.
nal_recv_from()
nal_send_to()
nal_close_socket()
nal_socket()
MD Users
socket()
close()
send_to()
recv_from()
Server
bind()
Socket
Setup
Send/
Receive
Resource
Cleaning

## Slide 13: General NAL Socket Usage [TCP]
TCP, connection based:
  Need to connect before data transferring.
Socket
Setup
Send/
Receive
Resource
Cleaning
socket()
close()
send()
recv()
bind()
nal_bind()
nal_connect()
nal_recv()
nal_send()
nal_close_socket()
nal_socket()
listen()
accept()
3-way handshaking
4-way handshaking
optional
MD Users
Server

## Slide 14: NAL Socket Usage
In general, the overall NAL socket usage is the same to common socket API.
But there are some extra notes to make MD networking applications workable:
  Specify incoming and outgoing interface (the PDN).
  Configure IPCore filters to receive packets in MD.
  Although MD TCP/IP stack supports both blocking/non-blocking socket:
    Due to MD behavior (RTOS), non-blocking socket is highly recommended.

## Slide 15: MD NAL Socket Usage [UDP]
nal_bind()
nal_recv_from()
nal_send_to()
nal_close_socket()
nal_setsockopt()
nal_socket()
nal_add_filter()
socket()
close()
send_to()
recv_from()
bind()
NAL_SO_BINDTODEVICE
Socket INFO
for filters
Delete filters
while closing socket
Connectionless:
  Pink color is for the interface and filter configurations.
MD Users
Server
Notes: Basically, its usage is the same as the socket API in common. The figure below gives a brief view about how to use it.

## Slide 16: How Does the Filter Work?
5-tuple filtering
+ PDN & PS ID
Use socket INFO to distinguish data to MD from data to AP.
5-tuple filtering: General socket INFO are SRC address, DEST address, protocol, SRC port and DEST port.
D
D
D
D
D
D
MD
AP
filter

## Slide 17: Data Transferring Overview
Nucleus socket layer
TCP/IP stack
nal_socket(protocol_type)
nal_bind(local_addr, ip_type)
nal_setsockopt(BINDTODEVICE, interface_id)
NAL SYS
MD users
NAL
allocate port
local addr
interface_id
stk_id
nal_add_filter(remote_addr)
socket operations
remote addr
protocol
ip_type
nal_sys_register_filter()
IPCore
...
filter (callback)
DL packets
pdn_id
ps_id
ipc_register_filter()
StkIF
StkIF
StkIF
UL packets
RX
...
ipc_uplink(…)
msg_send6(…,MSG_ID_D2CM_STKBRG_ESTABISHPDN_REQ,…)
STKIF driver
TX

## Slide 18: General NAL Socket Usage [TCP]
Connection based
socket()
close()
send()
recv()
Linux Server
bind()
nal_bind()
nal_connect()
nal_recv()
nal_send()
nal_close_socket()
Nucleus Client
nal_setsockopt()
nal_socket()
nal_add_filter()
listen()
accept()
3-way handshaking
4-way handshaking
NAL_SO_BINDTODEVICE
NAL_SO_LINGER (option)

## Slide 19: Tips to Debug --- Flow Overview
Issue
Setup PDN success?
Create socket success?
Bind success?
Set socket option success?
Filter success?
Root Cause
YES
YES
YES
PKTDUMP(ELT), Wireshark
NO
NO
NO
NO
NO
YES
YES
Error code
Is packet correct?
NO
TCP/IP logs
Find the fail stage
Check data flow: From the beginning to the fail stage
Fail stage found

## Slide 20: How to Find TCP/IP Related logs from ELT Trace?
Using “module ID” to find logs associated to TCP/IP components and tasks.
Module Name | NAL | STK Driver | TCP/IP Tasks
Module ID | NALDBG | STKDRV | STKDEMX/STKEVTD/STKBUF

## Slide 21: How to Check NAL Error Code ?
Using error code mapping table to get error messages.
FIL_NEED_BIND
Error Code Mapping
LINK

## Slide 22: Same Error code in Different Functions
Same error messages in different functions refer to different things.
NAL_INVALID_PARM
nal_get_sock_name
nal_connect
The input address is null or the input address length is invalid.
The server address is null or IP type is not IPv4 or IPv6.

## Slide 23: Check from the Data Transferring Flow --- UDP Uplink
Each stage would success only if stages before it succeed.
nal_send_to()
NAL_NO_DATA_TRANSFER
NAL_INVALID_SOCKET
NAL_WOULD_BLOCK
The socket is out of range.
Check if nal_socket() succeeded.
Check if the input is correct.
The non-blocking flag is set and there is no net buffer avalible.
Not a real error.
UDP send got an error and its not because out of buffer.
Check if the destination address is valid.
If nal_socket() got a real socket ID?
YES
<PART>
Error Code Table

## Slide 24: Check from the Data Transferring Flow --- UDP Downlink
The debugging logic is the same as uplink.
nal_recv_from()
NAL_NO_DATA_TRANSFER
NAL_NOT_CONNECTED
NAL_WOULD_BLOCK
The socket ID doesn’t point to a valid socket saved in the global socket structure.
The non-blocking flag is set and there is no packet recieved
Not an real error.
Read side channel has been closed.
Check if NAL_SHUT_RD/ NAL_SHUT_RDWR has set
nal_close_socket() has done?
<PART>
Error Code Table

## Slide 25: Case Study --- Cannot Connect to Server
Connect fail
Setup PDN success?
Create socket success?
Bind success?
Set socket option success?
Filter success?
YES
YES
NO
NO
NO
NO
NO
YES
YES
Error code
YES
Root Cause
PKTDUMP(ELT), Wireshark
Is packet correct?
NO
TCP/IP logs

## Slide 26: Check PDN Status
Compare to the fail case
What ELT trace shows…
MSG_ID_D2CM_STKBRG_ESTABLISHPDN_REQ
MSG_ID_D2CM_STKBRG_ESTABLISHPDN_CNF
SUCCESS!
success

## Slide 27: Check Socket Operation
No error has found.
SUCCESS!

## Slide 28: Is Filter Registration Success?
SUCCESS!
If it fails, an error code would return.
      PATH: mcu/common/interface/service/nal/ nal_public_defs.h

## Slide 29: Check Connecting Error Code
NAL_IS_CONNECTING Return value of non-blocking connection.
NAL_NO_DATA  None of the specified sockets is ready for data.
The client is still connecting to server.

## Slide 30: What to Do Next?
Till now, all socket operations are correct.
Check packet INFO  PKTDUMP
What else? TCP/IP logs
Filter success?
NO
YES
Root Cause
PKTDUMP(ELT), Wireshark
Is packet correct?
NO
TCP/IP logs

## Slide 31: Packet Dumping - Dump Stack Packets in ELT (1/3)
Steps:
  Launch ELT (after v2.1727.0).
  Load the saved *.elg file.
  Choose “External  Extract TCP/IP stack related packets only…”
    It will convert elg into pcapng files.
    A file with postfix, “pcapng”, would show up in the same folder.

## Slide 32: Packet Dumping - Dump Stack Packets in ELT (2/3)
List:
  The *.pcapng can be opened by Wireshark.
    You can check packet content in the tool.
  The “PS Index” in “Packet comments” can mapped to the specific log in ELT.
    You can also check the message “MSG_ID_STKBRG_PKTDUMP_REQ” in the ELT.

## Slide 33: Packet Dumping - Dump Stack Packets in ELT (3/3)
List:
  Wireshark usage:
    https://www.wireshark.org/docs/wsug_html_chunked/
  Packet headers:
    http://disruptivelabs.in/art-of-packet-crafting-with-scapy/networking/packet_headers/index.html
    Or google for more details.

## Slide 34: Look into other TCP/IP Logs
Find more logs near nal_connect().
  Check the handshaking status.

## Slide 35: Mapping logs to TCP/IP Log table
You find this among ELT logs.
What else INFO the log implies ?
LINK

## Slide 36: How To Debug?
MD Networking Applications
TCP/IP Stack
NAL
Users
Stack
[ELT log] Check PDN is established or not.
[ELT log] Check NAL socket usage is correct or not.
[ELT log] Check NAL API parameters.
[ELT log] Check filter configurations.
[ELT log + Map Table] Check NAL function return value.
[ELT log + Map Table] Check stack internal log messages.
[ELT log + PKTDUMP] Check packets dumping.
TCP/IP stack errors:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/MD%20TCPIP%20stack%20error%20message%20list.xlsx?Web=1
NAL programming guide:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/Gen93_NAL_Programming_Guide.docx?Web=1
NAL FAQ:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/Gen93_NAL_FAQ.docx?Web=1
NAL function return errors:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/NAL%20function%20return%20error%20code%20list.xlsx

## Slide 37: Case Study --- Socket Disconnection by BIP
Issue:
  The socket is disconnected by BIP unexpectedly.
Analysis:
  Check ELT log firstly  find some messages in the stack [map in table].
    Hit the threshold of retransmission times, close the connection.
    Stack will retry 5 times, 1s + 2s + 4s + 8s + 16s ~ total is 31 seconds.
  You can also check in the *.pcapng to see more packets details.
RST to close
connection

## Slide 38: Case Study --- BIP Link Drop
Issue:
  Link drop in BIP.
Analysis:
  Check ELT log firstly  find some messages in the stack [map in table].
    We see a message that “connection reset by foreign host”.
  You can also check in the *.pacpng to see more packets details.
    Got RST packet from BIP server
    Might need to cooperate with BIP to check why server sends this packet.
      Such as wrong BIP data, any fail, …

## Slide 39: Case Study --- BIP Timeout to Disconnect
Issue:
  Cannot setup socket connection  BIP timeout to disconnect  test case fail [CMCC].
Analysis:
  Check ELT log firstly  continue sending packets in ELT 
  Convert to *pcapng  Find that the packets are all SYN packets.
    TCP three handshake: SYN, SYN+ACK, ACK.
    No receive SYN+ACK from server.
       Server not response or IPCore not send/receive [advanced checking].
Establish
PDN
send one
packet

## Slide 40: Case Study --- BIP Link Drop (1/2)
Issue:
  Socket will disconnect unexpectedly.
Analysis:
  Check ELT log firstly:
    Got -257 in BIP NET MGR [map to table]  -257 means NAL_NOT_CONNECTED. (no connection)
    And PDN is disconnected later.

## Slide 41: Case Study --- BIP Link Drop (2/2)
Analysis (Cont’):
  Check *.pcapng:
    Got the FIN packet from server.
     So the connection is closed  disconnect on the socket to BIP.
  Cooperate with BIP to find that the BIP server might close the connection after1minute.
     FIN packet.

## Slide 42: Case Study --- BIP Server Not Response (1/2)
Issue:
  BIP server does not response after we send packet.
    IT3 + 8475 instrument GCF testing.
Analysis:
  Extension from the first case.
    Stack retries 5 times, then closing the connection.

## Slide 43: Case Study --- BIP Server Not Response (2/2)
Analysis (Cont’):
  Compare with PASS log, the MD stack might send the packets without PSH BIT.
  For the instrument testing, it seems we need to add PSH BIT for the testing.
  Final solution:
    Add PSH BIT to the last packet.
    Or TCP_NODELAY option.
Notes:   Two effects on this bit:
    The sending application informs TCP that data should be sent immediately.
       Some inputs and conditions, like no delay or timeout, to set this BIT.
    The PSH flag in the TCP header informs the receiving host that the data should be pushed up to the receiving application immediately.
  Conclusions:
    Without PSH bit, we still can receive ACK from Windows stack.
      Both Gemalto and NW+UE.
    With NO_DELAY option, it will add PSH bit and push every packets; otherwise, will be aggregated depended on MSS and TCP window.
    Receiver stack might have different configurations and implementations.
      At least, for instrument testing, it might need to set PSH flag for the ACK.

## Slide 44: Common Issue Type
List:
  PDN does not be established.
    MD interface is not up.
  Socket parameters are incorrect.
  Filter is configured wrong.
    No downlink packets.
  Cannot send out packets.
    GPD buffer full…
  Most issues are TCP cases:
    Cannot connect to server.
    Socket disconnection by server or local. (BIP link drop)
    …

## Slide 45: MD TCPIP Stack Debugging Guide - Reference Documents [Updating]
NAL programming guide:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/Gen93_NAL_Programming_Guide.docx?Web=1
NAL FAQ:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/Gen93_NAL_FAQ.docx?Web=1
NAL function return errors:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/NAL%20function%20return%20error%20code%20list.xlsx
TCP/IP stack errors:
  http://mtkteams.mediatek.inc/sites/WCT/Project/MT6293_MT6295/MT6293/Shared%20Documents/SW/35_Workshop/New_Features_SE7-D1/Day_2/MD_TCPIP/MD%20TCPIP%20stack%20error%20message%20list.xlsx?Web=1

## Slide 46: MD TCPIP Stack Debugging Guide - Contact
Module | Contact
NAL | Christine-PL Tsai
TCP/IP stack | Crilit Tu / I-Chih Lu
TCP/IP stack:
Module | Contact
BIP / BIP NET MGR | CS Huang / Actory Ou
D2NA / D2CM | Verit Chen / Chia-Yu Ku
IPCore | Peter Hsu / Bo-Kai Huang
Related modules:

## Slide 47: Q & A